## Slide 1
Stratus-HLS design flow manual
15 June 2017 Rev.2.0
Renesas System Design Co., Ltd. Design Methodology Dept.
Renesas Design Vietnam Co., Ltd. Front-end Dept.,
System Level Design Group

## Slide 2: Content
Introduction
Stratus-HLS design flow
        Overview
        Using ssgen
        SystemC description
        SystemC style check
        Behavioral synthesis
        SystemC-RTL equivalence check by Simulation based checker
        SystemC-RTL equivalence check by SLEC
Tools’ usages in Stratus-HLS flow
Referring documents

## Slide 3: 1. INTRODUCTION
Purpose of this guide
    This guide explains about following items to apply Stratus-HLS in High-level Design:
        High-level design flow using Stratus-HLS
        Tools used in Stratus-HLS flow
        Referring documents
What is Stratus-HLS?
    Stratus HLS is a behavioral synthesis tool from Cadence Design Systems in replacement of CtoS. It is believed to have better data path optimization than CtoS.

## Slide 4: 2. STRATUS-HLS DESIGN FLOW a. Overview (1)
SystemC design
SystemC style check
SystemC verification
Behavioral synthesis
RTL style check
SystemC-RTL equivalence check
SystemC-RTL co-verification
ssgen
1Team/SSChecker
OCSI/VCS/IES
Stratus
Spyglass
Simulation based checker/SLEC
VCS/IES
Specification
Design of SystemC model for behavioral synthesis
SystemC description style check
Functional and timing verification Code coverage measurement
Assertion based verification
RTL generation by behavioral synthesis
QoR improvement
Synthesized RTL description style check
Equivalence check between SystemC and synthesized RTL
Functional and timing verification by SystemC test-bench
This is an overall flow of High-level design using Stratus-HLS.

## Slide 5: 2. STRATUS-HLS DESIGN FLOW a. Overview (2)
Below phases in Stratus-HLS flow are described in this guide.
    Using ssgen
    SystemC description related to Stratus-HLS
    SystemC style check with SSChecker
    Behavioral synthesis with Stratus-HLS
    SystemC-RTL equivalence check
        By Simulation based Checker for pipeline synthesis
        By SLEC for cycle accurate synthesis
The others are almost similar to conventional CtoS flow. Refer to “High-level Design Flow Guide v2.1” (described in chapter 4) for detail.

## Slide 6: 2. STRATUS-HLS DESIGN FLOW b. Using ssgen
Below is an example for generation of all phases in Stratus-HLS flow. For more usage of ssgen, refer to “ssgen User’s Manual”.
Use ssgen v1.9.1 and later /common/appl/Renesas/SystemC/utility/ssgen/v1.9.1
$> ssgen.pl –in dut.in –stratus -ies -checker –sim_eq -slec –subdir
ssgen
Input files
Module information
Hierarchy information
Module templates
Testbench templates
Stratus execution scripts
IES execution scripts
for verification
Checkers execution scripts
Simulation based checker execution scripts for Equivalence check
-stratus
-ies
-checker
-sim_eq
(default)
Need to modify based on design
Can be
run without modification
SLEC scripts for Equivalence check
-slec
Note: -slec option for Stratus is only supported by ssgen v1.9.3 and later.

## Slide 7: 2. STRATUS-HLS DESIGN FLOW c. SystemC description (1)
The micro-arch constrains in Stratus-HLS are specified by directives in source code instead of tcl command.
Below are some directives frequently used. Examples are given in subsequent slides.
    HLS_DEFINE_PROTOCOL
    HLS_PIPELINE_LOOP
    HLS_CONSTRAIN_LATENCY
    HLS_DPOPT_REGION
    HLS_SCHEDULE_REGION
To get full list of supported directives, refer to “Stratus High-Level Synthesis Reference Guide” (described in chapter 4).

## Slide 8: 2. STRATUS-HLS DESIGN FLOW c. SystemC description (2)
HLS_DEFINE_PROTOCOL
    By default setting, “wait()” statement will be ignored by Stratus if it was not in HLS_DEFINE_PROTOCOL region.
void dut::thread_main() {
out0.write(0);
wait();
while (1) {
int x = in0.read();
out0.write(x);
wait(); } }
void dut::thread_main() {
{ HLS_DEFINE_PROTOCOL(“reset”)
out0.write(0);
wait();
}
while (1) {
{ HLS_DEFINE_PROTOCOL(“main”)
int x = in0.read();
out0.write(x);
wait();
} } }
Ignored
in default
Kept
Order of behaviors is not kept in default
in0.read() -> out0.write()
Pipeline synthesis only

## Slide 9: 2. STRATUS-HLS DESIGN FLOW c. SystemC description (3)
HLS_DEFINE_PROTOCOL (cont.)
    If the attribute “default_protocol” is on, “wait()” statement is kept by Stratus without HLS_DEFINE_PROTOCOL directive.
    In cycle accurate synthesis, the “default_protocol” attribute should be on.
void dut::thread_main() {
out0.write(0);
wait();
while (1) {
int x = in0.read();
out0.write(x);
wait(); } }
set_attr default_protocol yes
Kept
define_hls_module DUT BASIC --default_protocol=true
or
Pipeline synthesis only

## Slide 10: 2. STRATUS-HLS DESIGN FLOW c. SystemC description (4)
HLS_PIPELINE_LOOP and HLS_CONSTRAIN_LATENCY
    The HLS_PIPELINE_LOOP directive tells Stratus HLS to pipeline its enclosing loop.
    The HLS_CONSTRAIN_LATENCY directive is used to specify the minimum and maximum acceptable latency for a block of code (enclosed by {}).
    In pipeline synthesis, the “default_protocol” attribute must not be on.
    The directives will be generated in source file by ssgen if “-pipe” option is used for “cthread” command in input file.
void dut::thread_main() {
{ HLS_DEFINE_PROTOCOL(“reset”)
out0.write(0);
wait();}
while (1) {
HLS_PIPELINE_LOOP(HARD_STALL, 1, “PL_MAIN”);
int x,y,z;
{ HLS_DEFINE_PROTOCOL(“input”)
x = in0.read();
y = in1.read();}
{ HLS_CONSTRAIN_LATENCY(0, 10, “PL_MAIN_CONST”);
z = func(x,y);}
{ HLS_DEFINE_PROTOCOL(“output”)
out0.write(z);
wait();} } }
Pipeline while(1) loop,
interval specified with 2nd argument
Pipeline latency constrain:
Min latency = 0, max latency = 10
Input protocol: in0 and in1 are read in
same timing (stage 1)
Output protocol: out0 is written in
last stage
Pipeline synthesis only

## Slide 11: 2. STRATUS-HLS DESIGN FLOW c. SystemC description (5)
HLS_DPOPT_REGION
    This directive tells Stratus to do the data path optimization for the enclosing block. A optimal customized cell is created for these enclosing codes (Similar to not inline function in CtoS).
    This is especially helpful for logic that is used frequently in the overall design.
    There are several configuration for this directive. Refer “Stratus_HLS_Reference_Guide” for more detail.
    Some knowhow will be described in next page.
{
HLS_DPOPT_REGION(“myGate”);
a = b * c + d * 17;
tmp = b + d;
if ( e ) {
a = a + tmp;
}
}
...
... = a;
b
c
d
e
a
myGate

## Slide 12: 2. STRATUS-HLS DESIGN FLOW c. SystemC description (6)
HLS_DPOPT_REGION should not be used for:
    Whole algorithm or whole one function which is invoked from SC_CTHREAD (thread calls only one function) due to long running time and not give the best result.
    Functions with read/write accesses to ports/signals.
HLS_DPOPT_REGION should be defined for:
    Simple functions called from many different functions
    Simple functions used internal variables
HLS_DPOPT_REGION should be defined for operation cluster across multiple lines
    In complex functions where temporal variable is used.
    Temporal variable is parsed as function argument.

## Slide 13: 2. STRATUS-HLS DESIGN FLOW c. SystemC description (7)
HLS_SCHEDULE_REGION
    This directive tells Stratus to synthesize the operations in the specified region as if they are in a separated SC_CTHREAD, with an independent finite FSM.
    There are several configurations and restrictions for this directive. Refer “Stratus_HLS_Reference_Guide” for more detail.
    Some knowhow will be described in next page.
{
HLS_SCHEDULE_REGION(“mySubMod”);
a.write(b * c + d * 17);
wait();
tmp = b + d + a.read();
if ( e ) {
a.write(tmp);
}
wait();
}
b
c
d
e
a
mySubMod

## Slide 14: 2. STRATUS-HLS DESIGN FLOW c. SystemC description (8)
HLS_SCHEDULE_REGION should be used for:
    Functions has a variable latency.
    Functions has long latency.
    Functions has internal loop that will not be unrolled.
HLS_SCHEDULE_REGION should not be used for:
    Code blocks at the middle of functions.
    Functions without wait statement.
    Functions are not called from SC_CTHREAD.
    Functions are called in multiple SC_CTHREAD.

## Slide 15: 2. STRATUS-HLS DESIGN FLOW d. SystemC style check
Beside normal rules, SSChecker has two special rules for checking SystemC description related to Stratus-HLS.
    STRATUS_001: flags access to port/signal which is not enclosed by HLS_DEFINE_PROTOCOL directive.
    STRATUS_002: flags multiple access to ports/signals in same statements.
        As a recommendation from Cadence that HLS_DPOPT_REGION directives should not enclose read/write method.
        So this rule is introduced to optimize QoR of HLS_DPOPT_REGION directives.
To enable these rules, add option “-stratus” to command line option of SSChecker (automatically added to execution script by ssgen in this flow).
while (1) {
unsigned int in = din.read(); // Flagged by STRATUS_001
out = func(in);
{HLS_PROTOCOL_REGION(“output”);
dout.write(out); // Not flagged by STRATUS_001
wait();
} }
out0.write( in0.read() + in1.read()); // Flagged by STRATUS_002
int a = in0.read(); int b = in1.read(); // Not flagged by STRATUS_002
int c;
c= a + b;
out0.write(c); // Not flagged by STRATUS_002
$> SSChecker.pl dut.cpp –stratus

## Slide 16: 2. STRATUS-HLS DESIGN FLOW e. Behavioral synthesis (1)
Similar to conventional flow with CtoS, in this phase, the created SystemC model is automatically generated to RTL via behavior synthesis tool, Stratus-HLS.
What to do
    The execution scripts of Stratus-HLS can be automatically generated using ssgen.
    RTL is not generated if error occurs. Confirm the log file and generated RTL.
    Confirm functionality of generated RTL via “SystemC-RTL equivalence check” and confirm timing constrain, area constrain, wire congestion via “Logic synthesis”.
Stratus-HLS
project.tcl
Makefile
SystemC
descriptions
Cell libraries
RTL
Execution log

## Slide 17: 2. STRATUS-HLS DESIGN FLOW e. Behavioral synthesis (2)
Inputs:
    SystemC descriptions
    Synthesis scripts (Makefile, project.tcl)
    Cell libraries
Tools used:
    Stratus-HLS
    ssgen
    Logic synthesis tool (RTL Compiler or Design Compiler)
Outputs:
    RTL
    Execution log
Note:
    Micro-arch constrains in Stratus are specified by directives (in source code) instead of tcl command. Refer chapter 4 for more detail.
    Both cycle accurate (CA) and pipeline synthesis are supported.

## Slide 18: 2. STRATUS-HLS DESIGN FLOW e. Behavioral synthesis (3)
Stratus execution scripts generated by ssgen.
    By default, no option is required in execution of run_stratus.csh
    Specify “project_*.tcl” (one or more) for synthesizing target modules only.
    Specify “-gui” option to execute Stratus_IDE.
    Specify “-skip_ins” option to omit generation from cpp2ins. This option is available only if “-ins” option is used while executing ssgen.
    Specify “-cfg <HLS_CONFIG>” option to execute Stratus with other configuration (default is BASIC).
ssgen
dut.in
Stratus execution scripts
project_dut.tcl
Makefile_dut.stratus
run_stratus.csh
-stratus
$> run_stratus.csh [project_dut.tcl] [-gui] [-skip_ins] [-cfg <HLS_CONFIG>]

## Slide 19: 2. STRATUS-HLS DESIGN FLOW e. Behavioral synthesis (4)
Example
use_tech_lib “tutorial.lbr”
set_attr clock_period “5.0”
set_attr ...
...
define_hls_module DUT dut.cpp
define_hls_config DUT BASIC
define_logic_synthesis_config L {dut –all} –command bdw_runrc
MAKEFILE_PRJ = Makefile_dut.prj
$(MAKEFILE_PRJ) : project_dut.tcl
@bdw_makegen project_dut.tcl -o $(MAKEFILE_PRJ)
-include $(MAKEFILE_PRJ)
project_dut.tcl
Makefile_dut.stratus
%> bs –M 8000 make –f Makefile_dut.stratus hls_BASIC
%> bs –M 500 bdw_export –dutmodels RTL_V –libmodels RTL_V –combined_file dut.v –lsconfig L_BASIC rtl
rtl/dut.v
Cell library and clock period can be customized by specify following commands in ssgen input file:
  stratus_target_lib <cell library (full path)>
  stratus_period <clock period>

## Slide 20: 2. STRATUS-HLS DESIGN FLOW e. Behavioral synthesis (5)
Example (cont.)
stratus_hls 15.21-p100 (11111647)
Copyright (c) 2015 Cadence Design Systems, Inc. All rights reserved worldwide.
00481: -D is set to "STRATUS=1, STRATUS_HLS=1, CYNTHESIZER, CYNTHHL,
00481. STRATUS,
00481. BDW_RTL_dut_BASIC=1".
...
02974: Generated 12 gate enable expressions for 31 operations
02973: Optimize clock gating - process completed
01131: Scheduled constraint "PL_MAIN_CONST" in 3 cycle(s).
...
Execution log: bdw_work/modules/dut/BASIC/stratus_hls.log
Pipeline latency is 4.
  3 in PL_MAIN_CONST
  1 at bottom of while(1) loop (wait statement)
Pipeline synthesis only

## Slide 21: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (1)
In this phase, generated RTL by Stratus-HLS should be verified to be functionally equivalent to the SystemC descriptions.
    Method in this part is used for pipeline synthesis. For CA synthesis, please use SLEC.
A method is used to confirm validation of generated RTL via function/code coverage 100%.
    100% function coverage via SystemC-RTL co-simulation whose environment (test-bench, patterns, checker, etc.) is diverted from SystemC verification.
        This guide doesn’t mention function coverage. Refer to “High-level Design Flow Guide v2.1”.
    100% code coverage via confirming equivalency between SystemC-RTL with simulation based equivalence checker.
        This guide mentions code coverage from next page
Behavioral model
(SystemC)
Spec
Test
patterns
HLS
(Stratus)
SystemC
simulation
RTL
SC-RTL
simulation based equivalence check
RTL
simulation
Code coverage 100%
Function coverage 100%
RTL validation
Pipeline synthesis only

## Slide 22: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (2)
Flow of simulation based checker with IES and Jasper Gold (JG-UNR & JG-SEC or JG-SPV)
IES simulation
driver
monitor
RTL
SystemC
Coverage database
JG-UNR
JG-SEC/
JG-SPV
(1) Random
(6) Direct
(2)
(7)
(3)
(5)
(4)
reachable
conditions
unreachable
conditions
proven conditions
-> unreachable
    (1) IES simulation with random pattern
    (2) Generation of coverage database (for HLS RTL)
    (3) Formal reachability analysis for uncovered condition in (2) with JG-UNR
    (4) Formal path-sensitization analysis for reachable conditions in (3) with JG-SEC or JG-SPV
    (5) Conversion of generated VCDs to direct patterns
    (6) IES simulation with direct patterns
    (7) Update coverage database
Pipeline synthesis only

## Slide 23: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (3)
Inputs:
    SystemC descriptions
    Generated RTL
    Testbench and random pattern
    Simulation and support scripts
Tools used:
    ssgen
    IES (ncsim, ncverilog, imc)
    Jasper Gold (JG-UNR, JG-SEC or JG-SPV)
Outputs:
    RTL coverage report
    Simulation result
Note:
    All environment of simulation based equivalence checker can be generated automatically by ssgen. Refer next pages for more detail.
Pipeline synthesis only

## Slide 24: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (4)
Equivalence checker execution scripts generated by ssgen.
    By default, JG-SEC is used. If “-spv” is specified, JG-SPV is used. These two features has same result and no much difference in performance. JG-SEC is recommended to use since there are more licenses of JG-SEC than JG-SPV (3 vs. 1).
    Specify “jg_*.tcl” to execute target modules only.
    Contents of red color files can be varied by configuration in ssgen input file. See next page for more detail.
ssgen
dut.in
Equivalence checker execution scripts
run_sim_eq.csh
get_fanout.pl, vcd2tb.pl
imc_eq.cmd, cov.ccf
ncverilog_lsfsh
jg_dut_sec.tcl, jg_dut_spv.tcl
main_dut_eq.cpp, tb_dut_eq.cpp, tb_dut_eq.h, dut_stimulus.h
-sim_eq
$> run_sim_eq.csh [jg_dut.tcl] [-spv]
Pipeline synthesis only

## Slide 25: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (5)
ssgen configurations for equivalence checker (1/2)
    Some options of “uin/sin/uout/sout” commands are used to configure the equivalence checker.
Command | Option | Content of processing
uin/sin | -en [low¦high] | Input category options. There are four kind of input ports: Enable port: In testbench, it is clear before and after including random/direct patterns. In JG setting, it is constrained to be inactive after reset signal is de-asserted. In random pattern, it is cleared and set every certain number of cycles (*). Stall port: In testbench, it is clear before and after including random/direct patterns. In monitoring function, the output monitor progress is suspended if stall port is active. In JG setting, it is constrained to be inactive after reset signal is de-asserted. In random pattern, it is set to random value in every certain number of cycles (*). Register: Register input port is not touched in testbench and JG setting by default. It is set to random value in random pattern every certain number of cycles (*). Data: Data input port is not touched in testbench and JG setting but written with random value in random pattern every cycle. Only one of these options is allowed for each input port. Input port is treated as “Data” if none of them is specified. Active level can be set to enable/stall port. Default level is high if not specified. Array is not allowed for enable/stall port. (*) This number can be set by command “`define SIM_EQ_MAX_CNT N” (Default is 100 if not specified).
 | -stall [low¦high] | 
 | -reg | 
 | -data | 
Pipeline synthesis only

## Slide 26: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (6)
ssgen configurations for equivalence checker (2/2)
Command | Option | Content of processing
uin/sin | -en_sig <enable signal> | These options are used to constrain JG setting. They are available for enable/stall/register input ports. Constrained by “-en_sig”: Enable and stall ports are constrained to active if enable signal is asserted. Register ports are constrained to stable if enable signal is asserted. Constrained by “-dis_sig”: Enable and stall input ports are constrained to be clear if enable signal is asserted. Register ports are constrained to 0 if enable signal is asserted. Enable signal is input port which set as enable (-en).
 | -dis_sig <enable signal> | 
 | -dont_touch | This option is used to customize random pattern. It is only available for enable/stall input ports. Input port constrained by this option is not touched in random pattern.
 | -random | This option is used to customize random pattern. It is only available for enable input ports. Input port constrained by this option is set to random value every certain number of cycles. This number can be set by command “`define SIM_EQ_MAX_CNT N” (Default is 100 if not specified).
uout/sout | -en [low¦high] | Output category options. There are two kind of output ports: enable port and data port. Only one of these options is allowed for each output port. Output port is treated as “Data” if none of them is specified. In testbench, values of data ports are read based on corresponding enable port to compare b/w RTL and SystemC. In JG settings, check_sec/check_spv command are created for each set of output data ports which have same enable signal. Active level can be set to enable port. Default level is high if not specified. Array is not allowed for enable port.
 | -data [-en_sig <enable signal>] | 
Pipeline synthesis only

## Slide 27: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (7)
Example 1 – Basic (1/4): Testbench
module dut
clock clk
sreset rst_n neg
uinb in_en -en
uinb in_stall -stall
uin16 in_reg -reg –en_sig in_en
uin32 in_data -data
uoutb out_en -en
uout32 out_data -data –en_sig out_en
cthread main_thread
dut.in
...
void tb_dut_eq::thread_main() {
reset_function();
wait(10);
rst_n.write(1);
srand(0);
in_en.write(0);
in_stall.write(0);
wait();
#include "dut_stimulus.h“ // random pattern
in_en.write(0);
in_stall.write(0);
wait(3);
...
my_wait();
sc_stop();
my_wait();
}
void tb_dut_eq::thread_monitor() {
while (1) {
while (in_stall.read()) {
wait();
}
// scout0
if (out_en_s.read()) {
sc_uint<24> v_out_data_s = out_data_s.read();
fprintf(scout0, " %08x" , v_out_data_s.to_uint());
fprintf(scout0, "\n");
}
// rtlout0
if (out_en_r.read()) {
sc_uint<24> v_out_data_r = out_data_r.read();
fprintf(rtlout0, " %08x" , v_out_data_r.to_uint());
fprintf(rtlout0, "\n");
}
wait();
}
}
sim_eq/dut/tb_dut_eq.cpp
Pipeline synthesis only

## Slide 28: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (8)
module dut
clock clk
sreset rst_n neg
uinb in_en -en
uinb in_stall -stall
uin16 in_reg -reg –en_sig in_en
uin32 in_data -data
uoutb out_en -en
uout32 out_data -data –en_sig out_en
cthread main_thread
Example 1 – Basic (2/4): Random pattern
// "dut_stimulus.h"
wait(4);
for (int i=0; i<10000; i++) {
sc_uint<32> v_in_data;
v_in_data.range(31,16) = rand()%65536;
v_in_data.range(15,0) = rand()%65536;
in_data.write(v_in_data);
if (i%100==0) {
sc_uint<16> v_in_reg;
v_in_reg.range(15,0) = rand()%65536;
in_reg.write(v_in_reg);
}
wait();
}
in_en.write(1);
in_stall.write(1);
wait(3);
for (int i=0; i<50000; i++) {
if (i%100==0) {
in_en.write(0);
wait(rand()%4+1);
in_en.write(1);
in_stall.write(rand()%2);
}
sc_uint<32> v_in_data;
v_in_data.range(31,16) = rand()%65536;
v_in_data.range(15,0) = rand()%65536;
in_data.write(v_in_data);
if (i%100==0) {
sc_uint<16> v_in_reg;
v_in_reg.range(15,0) = rand()%65536;
in_reg.write(v_in_reg);
}
wait();
}
// end "dut_stimulus.h"
sim_eq/dut/dut_stimulus.h
dut.in
Pipeline synthesis only

## Slide 29: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (9)
Example 1 – Basic (3/4): Input constrains in JG tcl files
module dut
clock clk
sreset rst_n neg
uinb in_en -en
uinb in_stall -stall
uin16 in_reg -reg –en_sig in_en
uin32 in_data -data
uoutb out_en -en
uout32 out_data -data –en_sig out_en
cthread main_thread
dut.in
...
check_unr -setup -coverage all
clock dut0.clk
reset -expression ~dut0.rst_n -non_resettable_regs 0
assume -env -name C0 { $rose(dut0.rst_n) |-> dut0.in_en==0 }
assume -env -name C1 { $rose(dut0.rst_n) |-> dut0.in_stall==0 }
assume -env -name C2 { dut0.in_en==1 |-> $stable(dut0.in_reg) }
...
sim_eq/dut/jg_dut_sec.tcl or sim_eq/dut/jg_dut_spv.tcl
Pipeline synthesis only

## Slide 30: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (10)
Example 1 – Basic (4/4): Output related setting in JG tcl files
module dut
clock clk
sreset rst_n neg
uinb in_en -en
uinb in_stall -stall
uin16 in_reg -reg –en_sig in_en
uin32 in_data -data
uoutb out_en -en
uout32 out_data -data –en_sig out_en
cthread main_thread
dut.in
...
check_sec -map -spec { dut0.out_data } -spec_condition { dut0.out_en==1 } -global
...
set prv_list ""
set n 1
foreach b $cov_list {
if { [string match "*precondition*" $b]==0 } {
set spv_status [get_property_info -list status spv_${n}::dut0.out_data\[23:0\] ]
puts "spv_$n $spv_status"
if {[string match "proven" $spv_status]==1} {
append prv_list " $b"
}
incr n
}
}
...
...
set spv_cmd_0 "check_spv -create -name spv_${n}_0 -from ${sig_list} -from_precond {$b==1} -to { dut0.out_data } -to_precond { dut0.out_en==1 }"
puts "$spv_cmd_0"
eval $spv_cmd_0
...
set cex_cmd_0 "check_spv -create -name spv_${n}_0_cex -from ${sig_list} -from_precond {$b==1} -to { dut0.out_data } -to_precond { dut0.out_en==1 }"
puts "$cex_cmd_0"
eval $cex_cmd_0
...
sim_eq/dut/jg_dut_sec.tcl
sim_eq/dut/jg_dut_spv.tcl
Pipeline synthesis only

## Slide 31: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (11)
Example 2 – Advanced (1/4): Testbench
`define SIM_EQ_MAX_CNT 250
module dut
clock clk
sreset rst_n neg
uinb in_en_0 -en -random
uinb in_en_1n -en low -dis_sig in_en_0
uinb in_en_2 -en -dont_touch
uinb in_stall -stall
uin32 in_data
uoutb out_en_0n -en low
uout32 out_data_0 -data -en_sig out_en_0n
cthread main_thread
dut.in
...
void tb_dut_eq::thread_monitor() {
while (1) {
while (in_stall.read()) {
wait();
}
// scout0
if (!out_en_0n_s.read()) {
sc_uint<32> v_out_data_0_s = out_data_0_s.read();
fprintf(scout0, " %08x" , v_out_data_0_s.to_uint());
fprintf(scout0, "\n");
}
// rtlout0
if (!out_en_0n_r.read()) {
sc_uint<32> v_out_data_0_r = out_data_0_r.read();
fprintf(rtlout0, " %08x" , v_out_data_0_r.to_uint());
fprintf(rtlout0, "\n");
}
wait();
}
}
Testbench: sim_eq/dut/tb_dut_eq.cpp
Pipeline synthesis only

## Slide 32: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (12)
Example 2 – Advanced (2/4): Random pattern
`define SIM_EQ_MAX_CNT 250
module dut
clock clk
sreset rst_n neg
uinb in_en_0 -en -random
uinb in_en_1n -en low -dis_sig in_en_0
uinb in_en_2 -en -dont_touch
uinb in_stall -stall
uin32 in_data
uoutb out_en_0n -en low
uout32 out_data_0 -data -en_sig out_en_0n
cthread main_thread
dut.in
// "dut_stimulus.h"
wait(4);
for (int i=0; i<10000; i++) {
sc_uint<32> v_in_data;
v_in_data.range(31,16) = rand()%65536;
v_in_data.range(15,0) = rand()%65536;
in_data.write(v_in_data);
wait();
}
in_en_0.write(1);
in_en_1n.write(0);
in_en_2.write(1);
in_stall.write(1);
wait(3);
for (int i=0; i<50000; i++) {
if (i%250==0) {
in_en_0.write(0);
in_en_1n.write(1);
wait(rand()%4+1);
in_en_0.write(rand()%2);
in_en_1n.write(0);
in_stall.write(rand()%2);
}
sc_uint<32> v_in_data;
v_in_data.range(31,16) = rand()%65536;
v_in_data.range(15,0) = rand()%65536;
in_data.write(v_in_data);
wait();
}
// end "dut_stimulus.h"
Random pattern: sim_eq/dut/dut_stimulus.h
in_en_2 is not written in 2nd loop of random pattern
Pipeline synthesis only

## Slide 33: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (13)
Example 2 – Advanced (3/4): Input constrains in JG tcl files
`define SIM_EQ_MAX_CNT 250
module dut
clock clk
sreset rst_n neg
uinb in_en_0 -en -random
uinb in_en_1n -en low -dis_sig in_en_0
uinb in_en_2 -en -dont_touch
uinb in_stall -stall
uin32 in_data
uoutb out_en_0n -en low
uout32 out_data_0 -data -en_sig out_en_0n
cthread main_thread
dut.in
...
check_unr -setup -coverage all
clock dut0.clk
reset -expression ~dut0.rst_n -non_resettable_regs 0
assume -env -name C0 { $rose(dut0.rst_n) |-> dut0.in_en_0==0 }
assume -env -name C1 { $rose(dut0.rst_n) |-> dut0.in_en_2==0 }
assume -env -name C2 { $rose(dut0.rst_n) |-> dut0.in_stall==0 }
assume -env -name C3 { dut0.in_en_0==1 |-> dut0.in_en_1n==1 }
...
sim_eq/dut/jg_dut_sec.tcl or sim_eq/dut/jg_dut_spv.tcl
Pipeline synthesis only

## Slide 34: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (14)
Example 2 – Advanced (4/4): Output related setting in JG tcl files
`define SIM_EQ_MAX_CNT 250
module dut
clock clk
sreset rst_n neg
uinb in_en_0 -en -random
uinb in_en_1n -en low -dis_sig in_en_0
uinb in_en_2 -en -dont_touch
uinb in_stall -stall
uin32 in_data
uoutb out_en_0n -en low
uout32 out_data_0 -data -en_sig out_en_0n
cthread main_thread
dut.in
...
check_sec -map -spec { dut0.out_data_0 } -spec_condition { dut0.out_en_0n==0 } –global
...
sim_eq/dut/jg_dut_sec.tcl
...
set spv_cmd_0 "check_spv -create -name spv_${n}_0 -from ${sig_list} -from_precond {$b==1} -to { dut0.out_data_0 } -to_precond { dut0.out_en_0n==0 }"
puts "$spv_cmd_0"
eval $spv_cmd_0
...
set cex_cmd_0 "check_spv -create -name spv_${n}_0_cex -from ${sig_list} -from_precond {$b==1} -to { dut0.out_data_0 } -to_precond { dut0.out_en_0n==0 }"
puts "$cex_cmd_0"
eval $cex_cmd_0
sim_eq/dut/jg_dut_spv.tcl
Pipeline synthesis only

## Slide 35: 2. STRATUS-HLS DESIGN FLOW f. SystemC-RTL equivalence check by Simulation based checker (15)
Example of equivalence checker result
Mon Jun 13 12:08:51 ICT 2016
No mismatch 0 @ Random
No mismatch 0 @ trace/spv_1_0_cex.vcd
Simulation result: sim_eq/dut/result_*.log
No mismatch in simulation
name Block Branch Statement Expression Toggle Fsm Average Fsm Covered
--------------------------------------------------------------------------------------------------------------------------------
sc_main n/a n/a n/a n/a n/a n/a n/a
|--dut0 100.00% (...) 100.00% (...) 100.00% (...) 100.00% (...) 100.00% (...) n/a n/a
<><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><><>
...
Report date: Mon 13 Jun 2016 12:14:02 ICT
Coverage report: sim_eq/dut/imc_cov_eq_*.log
RTL code coverage is 100%
Pipeline synthesis only

## Slide 36: 2. STRATUS-HLS DESIGN FLOW g. SystemC-RTL equivalence check by SLEC
SLEC execution scripts generated by ssgen.
    By default, no option is required in execution of run_slec_st.csh
    Specify “slec_*_st.tcl” (one or more) for target modules only.
    Specify “-skip_ins” option to omit generation from cpp2ins. This option is available only if “-ins” option is used while executing ssgen.
    The report of SLEC is similar to those for CtoS-RTL. Refer to “High-level Design Flow Guide v2.1”.
ssgen
dut.in
SLEC execution scripts
run_slec_st.csh
slec_st_lsfsh
slec_dut_st.tcl
-stratus -slec
$> run_slec_st.csh [slec_dut_st.tcl] [-skip_ins]
Cycle accurate synthesis only

## Slide 37: 3. TOOLS USED IN STRATUS-HLS FLOW
No. | Tool name | Version | Vendor | Function | Intended phase
1 | Stratus-HLS | v16.23-p100 and later | Cadence | Behavioral synthesis tool | Behavioral synthesis
2 | JasperGold | v15.12.000 | Cadence | Verification platform | SystemC-RTL equivalence check
3 | 1Team:System | v1.16.7 | Synopsys | SystemC description check tool | SystemC description check
4 | Spyglass | v5.4.1 | Synopsys | RTL description check tool | RTL description check
5 | IES | 15.20-s020 and later | Cadence | Logic simulator | SystemC verification SystemC-RTL co-verification SystemC-RTL equivalence check
6 | VCS-MX | 2016.06-sp2 and later | Synopsys | Logic simulator | SystemC verification SystemC-RTL co-verification
7 | OSCI | 4.1.2 or 4.2.2 | Freeware | C/C++/SystemC compiler | SystemC verification
8 | ssgen | v1.9.3 and later | Renesas | HLD assistance tool | All phases
9 | SSChecker | v3.2.1 and later | Renesas | SystemC description style checker | SystemC description check
10 | cpp2ins | v1.6 and later | Renesas | Coverage measurement support utility | SystemC verification
11 | SLEC | slec-7.1j | Mentor | Sequential Logic Equivalence Checker | SystemC-RTL equivalence check
Following table lists the tools used in Stratus-HLS flow. It is recommended to use ssgen for automatic generation of SystemC description and execution scripts of all phases.

## Slide 38: 4. REFERENCE DOCUMENTS
This chapter only lists documents which are mentioned in this documents. For completed list of documents for High-Level design, refer to [1] below.
    High-Level Design Flow Guide, Rev. 2.1 【 REL intranet 】/【REL EDA Tools Information】/【System Level Design Guide】/ 【Manual】
    High-Level design supporting tool ssgen user's manual, v1.8 【 REL intranet 】/【REL EDA Tools Information】/【System Level Design Guide】/ 【Manual】
    Stratus High-Level Synthesis Reference Guide, v16.23 <Stratus install path>/doc/Stratus_HLS_Reference_Guide
    Stratus High-Level Synthesis User Guide, v16.23 <Stratus install path>/doc/Stratus_HLS_Reference_Guide
      About <Stratus install path>, please contact to 'shintaro.imamura.ry@renesas.com’

## Slide 39
www.renesas.com
Rev. | Modification content | Approved by | Reviewed by | Created by
1.0 | Newly created | Tetsuya Asano 07/27/2016 | Shintaro Imamura 07/26/2016 | Hiep Nguyen 07/26/2016
2.0 | Revise chapter 2.b ssgen support generating SLEC execution scripts Add chapter 2.g to add Stratus-SLEC flow Update version of tools used in Stratus-HLS design flow |  |  | Hong Lam 06/15/2017