## Slide 1
SSGen enhancement
  2018/Q1
  Version 1.1
01/29/2018
IP design 2 GROUP
Mcu CORE & IP SOLUTION 2 SECTION
FRONTEND DESIGN 2 DEPARTMENT
Hardware Engineer Division
Renesas Design Vietnam Co., Ltd

## Slide 2
Page 2
History
Version | Description | P.I.C
1.0 | Create new | Yen Nguyen 01/29/2018
1.1 | - Revise “-clk”, “-rst” option description - Change “-if_rst” to “-th” option enhancement - Revise AXI slave I/F description - Add monitor.v and map files description | Yen Nguyen 02/08/2018
1.2 | - p5: Add “-th” option enhancement for [u/s]outN - p7,12,14: Change ResetSync = true/false depend on sreset/areset - p7,12,14: Change ResetLevel = true/false depend on pos/neg of [s/a]reset - p11: Remove mask_data - p16: Add specification for traits when user specified multi different configuration for channels - p20: Add return for function return Boolean. - p32,33: Update example specification for “sim_eq” of struct issue to add d2[2] | Yen Nguyen 02/09/2018

## Slide 3: Agenda
Generation of SystemC using AXI/APB4 Stratus SytemC library
Preprocessor for “bind” and “mem
Fix “struct” issues
      Fix SLEC issue
      Fix sim_eq issue

## Slide 4
Page 4
1. Generation of SC using AXI/APB4 Stratus SC library
New command specification. This command will be used after module/top command as an attribute of module.
      {axi3|axi4|apb4}_{master|slave} ChannelName [options]:
        ChannelName: Name of instantiation of AXI3/AXI4/APB4 library
        -rst ResetName: Reset port name. SSGen will terminate with error if there is no reset command in .in file. User don’t need to specify “-rst” if the module has only one reset.
        -clk ClockName: Clock port name. SSGen will terminate with error if there is no clock command in .in file. User don’t need to specify “-clk” if the module has only one clock.
        -dw DataWidth: data width (bytes). Default: 4
        -aw AddressWidth: address width (bytes). Default: 4
        -uw UserWidth: user width (bits), used for AXI4 only. Default: 32
        -iw IDWidth: address ID width (bits), used for AXI. Default: 4
        -sw SizeWidth: burst size width (bits), used for AXI. Default: 3
Update v1.1

## Slide 5
Page 5
1. Generation of SC using AXI/APB4 Stratus SC library
“tap” and “bind” command are enhanced to support APB4/AXI I/F connection.
      tap [instancename.]ChannelName [ChannelName]: If ChannelName is not specified, default name is same as module channel name.
      bind master slave [ChannelName]: If channel is not specified, default name is “master_to_slave”
Enhance “-th” option for [u/s]regN, [u/s]outN command :
      Enhance option “-th” to notify that signal will be reset in APB4 Bus I/F reset function (to avoid multi-driven issue). SSGen will generate reset code into “reset_single_write” function.
        [u/s]regN -th <channel name>
      SSGen will terminate with error if channel name is not defined.
Update v1.2

## Slide 6
Page 6
1. Generation of SC using AXI/APB4 Stratus SC library
SSGen will generate:
      Traits specification files (apb4/axi3/axi4_traits.h)
      Corresponding monitor.v module & .map files.
      Added description in generated SystemC code:
        Instantiation APB4/AXI3/AXI4 library
        Related functions of APB4/AXI3/AXI4 library
        Connection of APB4/AXI3/AXI4 channels.
module test
clock PCLK
sreset PRESET pos
apb4_slave target1
uregb START
ureg16 CKS
ureg32 CNT
ureg32 COR -init 0xFFFFFFFF
uoutb INT
cthread main_thread -reset_header -wait_header
test.in
Update v1.1

## Slide 7
Page 7
1.1. Generation of SC using APB4 Stratus SC library
Traits specification file generation
    For APB4: file name: apb4_traits.h
#ifndef __APB4_TRAITS_H__
#define __APB4_TRAITS_H__
#include "cynw_apb4.h"
#include "cynw_tlm/cynw_tlm.h"
using namespace apb4;
#ifdef MAP_APB4_SIGNAL
static const bool sig_level = true;
#else
static const bool sig_level = false;
#endif
struct FAST_TLM_TRAITS : public SIG_TRAITS
{
static const bool Level = 0; // configures flex channels for TLM level
};
struct SIG_TRAITS_RESET : public SIG_TRAITS
{
static const bool ResetData = true;
static const bool ResetSync = true;
static const bool ResetLevel = true;
};
apb4_traits.h
typedef apb4_width_traits_default apb4_width_traits_default;
struct apb4_def_traits: public apb4_width_traits_default {
static const unsigned data_bytes = 4;
static const unsigned addr_bytes = 4;
};
struct apb4_def_traits : public apb4_traits_template<apb4_def_traits> {
#if defined(MAP_APB4_SIGNAL)
static const int io_config = IO_CONFIG_APB4_SIG;
typedef SIG_TRAITS_RESET put_get_traits;
#else
static const int io_config = IO_CONFIG_TLM1;
typedef FAST_TLM_TRAITS put_get_traits;
#endif
};
typedef apb4_initiator<apb4_def_traits> initiator1_t;
typedef apb4_b_initiator<apb4_def_traits> initiator1_b_t;
typedef apb4_target<apb4_def_traits> target1_t;
typedef apb4_single_rw_adaptor<apb4_def_traits> single_adaptor1_t;
typedef apb4_def_traits::tlm_traits::awchan_t awchan_t;
typedef apb4_def_traits::tlm_traits::wchan_t wchan_t;
typedef apb4_def_traits::tlm_traits::bchan_t bchan_t;
typedef apb4_def_traits::tlm_traits::archan_t archan_t;
typedef apb4_def_traits::tlm_traits::rchan_t rchan_t;
typedef hier_apb4_initiator<apb4_def_traits> hier_initiator1_t;
typedef hier_apb4_target<apb4_def_traits> hier_target1_t;
#endif
apb4_traits.h
Update v1.2
ResetSync = true/false depend on sreset/areset
ResetLevel = true/false depend on pos/neg of [s/a]reset

## Slide 8
1.1.1. Generation of APB4 Master i/F
APB4 Master I/F generation:
    For APB4: add descriptions in module header file
#include <systemc.h>
#include "ssgenlib.h"
#include “apb4_traits.h“
SC_MODULE(master) {
sc_in < bool > PCLK;
…
initiator1_b_t initiator1;
SC_CTOR(master)
: PCLK("PCLK")
…
, initiator1("initiator1")
{
initiator1.clk_rst(PCLK, PRESET);
…
}
void reset_main_thread() {
initiator1.awchan->reset_put();
initiator1.wchan->reset_put();
initiator1.bchan->reset_get();
initiator1.archan->reset_put();
initiator1.rchan->reset_get();
}
void apb4_read(unsigned addr);
void apb4_write (unsigned addr, unsigned data, unsigned strb = 0xF);
module master
clock PCLK
sreset PRESET pos
apb4_master initiator1 -clk PCLK -rst PRESET
uinb trig
cthread main_thread -reset_header -wait_header
master.in
src/master.h
ssgen.pl -in test.in

## Slide 9
1.1.1. Generation of APB4 Master i/F
APB4 Master I/F generation: (cont.)
    For APB4: add descriptions in module implementation file
void master::main_thread() {
…
while (1) {
…
apb4_write(1, 1);
wait(2);
…
}
void master::apb4_write(unsigned addr, unsigned data, unsigned strb) {
awchan_t v_awchan; // awchan
wchan_t v_wchan; // wchan
bchan_t v_bchan; // bchan
v_awchan.addr = addr;
v_wchan.data = data;
v_wchan.strb = strb;
// Write
v_bchan = initiator1.write(v_awchan, v_wchan);
}
void master::apb4_read(unsigned addr) {
archan_t v_archan; // archan
rchan_t v_rchan; // rchan
v_archan.addr = addr; // Addr
// Read
v_rchan = initiator1.read(v_archan);
}
module master
clock PCLK
sreset PRESET pos
apb4_master initiator1 -clk PCLK -rst PRESET
uinb trig
cthread main_thread -reset_header -wait_header
master.in
src/master.cpp
ssgen.pl -in test.in
Implementation by designer

## Slide 10
1.1.2. Generation of APB4 slave i/F
APB4 Slave I/F generation:
    For APB4: add descriptions in module header file
module test
clock PCLK
sreset PRESET pos
apb4_slave target1 -clk PCLK -rst PRESET
uregb START -if_rst
ureg32 COR -init 0xFFFFFFFF -if_rst
uoutb INT
cthread main_thread -reset_header -wait_header
test.in
src/test.h
…
#include “apb4_traits.h“
class test: public sc_module, apb4_single_rw_if<apb4_def_traits> {
sc_in < bool > PCLK;
…
// For APB4 I/F
single_adaptor1_t target1_adaptor;
target1_t target1;
SC_CTOR(test)
: PCLK("PCLK")
…
, CTOR_NM(target1)
, CTOR_NM(target1_adaptor)
{
target1.clk_rst(PCLK, PRESET);
target1.target_port(target1_adaptor);
target1_adaptor.target_port(*this);
…
}
(cont.)
void reset_main_thread() {
INT.write(0);
}
virtual bool can_single_read() const { return true; }
virtual bool can_single_write() const { return true; }
virtual void reset_single_read() {}
virtual void reset_single_write() {
START.write(0);
…
COR.write(0xFFFFFFFF);
}
virtual void single_read(archan_t& archan, rchan_t& rchan);
virtual void single_write(awchan_t& awchan, const wchan_t& wchan, bchan_t& bchan);
unsigned mask_data (unsigned cur_data, unsigned w_data, unsigned strb);
Signals, which are written in single_write will be reset in reset_single_write

## Slide 11
1.1.2. Generation of APB4 slave i/F
APB4 Slave I/F generation: (cont.)
    For APB4: add descriptions in module implementation file
src/test.cpp
unsigned apb4func::mask_data(unsigned cur_data, unsigned w_data, unsigned strb)
{
unsigned data = cur_data;
for (unsigned int i = 0; i < 4; i++) {
if ( (strb & (0x1 << i)) != 0 ) {
data = data & (~(0xFF << (i*8)));
data = data | (w_data & (0xFF << (i*8) ) ) ;
}
}
return data;
}
void apb4func::single_read(archan_t& archan, rchan_t& rchan)
{
// please write here
}
void apb4func::single_write(awchan_t& awchan, const wchan_t& wchan, bchan_t& bchan) {
bchan.error = false;
// please write here
…
}
module test
clock PCLK
sreset PRESET pos
apb4_slave target1 -clk PCLK -rst PRESET
uregb START -th reset_single_write
ureg32 COR -init 0xFFFFFFFF -th reset_single_write
uoutb INT
cthread main_thread -reset_header -wait_header
test.in
ssgen.pl -in test.in
Update v1.2
Not need to generate this code.
It should be depended on user.

## Slide 12
Page 12
1.2 Generation of SC using AXI Stratus SC library
Traits specification file generation
    For AXI3: file name: axi3_traits.h
#ifndef __AXI3_TRAITS_H__
#define __AXI3_TRAITS_H__
#include "cynw_axi3.h“
#include "cynw_tlm/cynw_tlm.h"
using namespace axi3;
#ifdef MAP_TLM2
#include "cynw_bus_interfaces/simple_bus/tlm2_transactors.h"
#include "cynw_bus_interfaces/axi3/axi3_tlm2.h"
#endif
#ifdef MAP_AXI3_SIGNAL
static const bool sig_level = true;
#else
static const bool sig_level = false;
#endif
struct FAST_TLM_TRAITS : public SIG_TRAITS
{
static const bool Level = 0; // configures flex channels for TLM level
};
struct SIG_TRAITS_RESET : public SIG_TRAITS
{
static const bool ResetData = true;
static const bool ResetSync = true;
static const bool ResetLevel = true;
};
axi3_traits.h
struct axi_def_bw_traits {
static const unsigned data_bytes = 8;
static const unsigned addr_bytes = 4;
static const unsigned default_size = 3;
static const unsigned SIZE_W = 3;
static const unsigned ID_W = 4;
};
template<typename simple_bus_traits_base>
struct axi3_def_traits
{
typedef axi3_traits<axi3_types_traits<axi3_width_traits<simple_bus_traits_base> > > tlm_traits;
#ifdef MAP_AXI3_SIGNAL
typedef axi3_traits<axi3_types_traits<axi3_width_traits<simple_bus_traits_base> > > hw_bus_traits;
#endif
#if defined(MAP_TLM2)
static const int io_config = IO_CONFIG_TLM2;
typedef FAST_TLM_TRAITS put_get_traits;
#elif defined(MAP_AXI3_SIGNAL)
static const int io_config = IO_CONFIG_AXI3_SIG;
typedef SIG_TRAITS_RESET put_get_traits;
#else
static const int io_config = IO_CONFIG_TLM1;
typedef FAST_TLM_TRAITS put_get_traits;
#endif
};
axi3_traits.h
Corresponding to “axi3_master/slave” option value
Update v1.2
ResetSync = true/false depend on sreset/areset
ResetLevel = true/false depend on pos/neg of [s/a]reset

## Slide 13
Page 13
1.2 Generation of SC using AXI Stratus SC library
Traits specification file generation
    For AXI3: file name: axi3_traits.h (cont.)
axi4_traits.h
….
typedef axi3_def_traits<axi_def_bw_traits> axi3_def_traits;
typedef axi3_initiator<axi_def_traits> initiator1_t;
typedef axi3_target<axi_def_traits> target1_t;
typedef axi3_def_traits::tlm_traits::awchan_t awchan_t;
typedef axi3_def_traits::tlm_traits::wchan_t wchan_t;
typedef axi3_def_traits::tlm_traits::bchan_t bchan_t;
typedef axi3_def_traits::tlm_traits::archan_t archan_t;
typedef axi3_def_traits::tlm_traits::rchan_t rchan_t;
typedef hier_axi3_initiator<axi3_def_traits> hier_initiator1_t;
typedef hier_axi3_target<axi3_def_traits> hier_target1_t;
#endif
axi4_traits.h
Update v1.1

## Slide 14
Page 14
1.2 Generation of SC using AXI Stratus SC library
Traits specification file generation
    For AXI4: file name: axi4_traits.h
#ifndef __AXI4_TRAITS_H__
#define __AXI4_TRAITS_H__
#include "cynw_axi4.h"
#include "cynw_tlm/cynw_tlm.h"
using namespace axi4;
#ifdef MAP_AXI4_SIGNAL
static const bool sig_level = true;
#else
static const bool sig_level = false;
#endif
struct FAST_TLM_TRAITS : public SIG_TRAITS
{
static const bool Level = 0; // configures flex channels for TLM level
};
struct SIG_TRAITS_RESET : public SIG_TRAITS
{
static const bool ResetData = true;
static const bool ResetSync = true;
static const bool ResetLevel = true;
};
typedef axi4_width_traits_default axi_width_traits_default;
….
axi4_traits.h
…
struct axi4_def_bw_traits: public axi_width_traits_default {
static const unsigned data_bytes = 8;
static const unsigned addr_bytes = 4;
static const unsigned default_size = 3;
static const unsigned SIZE_W = 3;
static const unsigned ID_W = 4;
};
struct axi4_def_userw_traits {
static const unsigned AWUSER_W = 32;
static const unsigned WUSER_W = 32;
static const unsigned BUSER_W = 32;
static const unsigned ARUSER_W = 32;
static const unsigned RUSER_W = 32;
};
struct axi4_def_traits : public axi4_traits_template<axi4_def_bw_traits, axi4_def_userw_traits> {
#if defined(MAP_TLM2)
static const int io_config = IO_CONFIG_TLM2;
typedef FAST_TLM_TRAITS put_get_traits;
#elif defined(MAP_AXI4_SIGNAL)
static const int io_config = IO_CONFIG_AXI4_SIG;
typedef SIG_TRAITS_RESET put_get_traits;
#else
static const int io_config = IO_CONFIG_TLM1;
typedef FAST_TLM_TRAITS put_get_traits;
#endif
};
axi4_traits.h
Corresponding to “axi4_master/slave” options value
ResetSync = true/false depend on sreset/areset
ResetLevel = true/false depend on pos/neg of [s/a]reset
Update v1.2

## Slide 15
Page 15
1.2 Generation of SC using AXI Stratus SC library
Traits specification file generation
    For AXI4: file name: axi4_traits.h (cont.)
axi4_traits.h
….
typedef axi4_initiator<axi4_def_traits> initiator1_t;
typedef axi4_target<axi4_def_traits> target1_t;
typedef axi4_def_traits::tlm_traits::awchan_t awchan_t;
typedef axi4_def_traits::tlm_traits::wchan_t wchan_t;
typedef axi4_def_traits::tlm_traits::bchan_t bchan_t;
typedef axi4_def_traits::tlm_traits::archan_t archan_t;
typedef axi4_def_traits::tlm_traits::rchan_t rchan_t;
typedef hier_axi4_initiator<axi4_def_traits> hier_initiator1_t;
typedef hier_axi4_target<axi4_def_traits> hier_target1_t;
#endif
axi4_traits.h

## Slide 16
Page 16
1.2 Generation of SC using AXI Stratus SC library
Traits specification file generation: if user specified multi different configuration of channels
    For options for than “-rst” and “-clk” options: beside default traits struct, the additional traits struct will be generated for each configuration.
    axi3/4_def_traits[_<option_nameN><option_valueN>]
    For example:
axi4_def_bw_traits_dw4_aw4: public axi_width_traits_default
axi4_def_bw_traits_dw8_aw8: public axi_width_traits_default
struct axi4_def_userw_traits_uw16 { …}
axi4_def_traits_dw4_aw4 : public axi4_traits_template<axi4_def_bw_traits_dw4_aw4, axi4_def_userw_traits>
axi4_def_traits_dw8_aw8_uw16 : public axi4_traits_template<axi4_def_bw_traits_dw4_aw4, axi4_def_userw_traits_uw16>
typedef axi4_initiator<axi4_def_traits_dw4_aw4> initiator1_dw4_aw4_t;
typedef axi4_target<axi4_def_traits_dw4_aw4> target1_dw4_aw4_uw16_t;
typedef axi4_initiator<axi4_def_traits_dw8_aw8_uw16> initiator1_dw8_aw8_uw16_t;
typedef axi4_target<axi4_def_traits_dw8_aw8_uw16> target1_dw8_aw8_uw16_t;
…
axi4_traits.h
Add v1.2
axi4_master initiator1 -dw 4 -aw 4
axi4_master initiator2 -dw 8 -aw 8 -uw 16

## Slide 17
1.2.1. Generation of Axi Master i/F
AXI3/4 Master I/F generation:
    Descriptions in module header file:
…
#include “axi3/4_traits.h“
SC_MODULE(master) {
sc_in < bool > ACLK;
…
initiator1_t initiator1;
SC_CTOR(master)
: PCLK("PCLK")
…
, initiator1("initiator1")
{
initiator1.clk_rst(ACLK, ARESET);
…
}
void reset_main_thread() {
initiator1.awchan->reset_put();
initiator1.wchan->reset_put();
initiator1.bchan->reset_get();
initiator1.archan->reset_put();
initiator1.rchan->reset_get();
}
module master
clock ACLK
sreset ARESET pos
axi3/4_master initiator1 -clk ACLK -rst ARESET
uinb trig
uoutb done
cthread main_thread -reset_header -wait_header
master.in
src/master.h
ssgen.pl -in master.in

## Slide 18
1.2.1. Generation of axi3 Master i/F
AXI3/4 Master I/F generation: (cont.)
    Descriptions in module implementation file
module master
clock ACLK
sreset ARESET pos
axi3/4_master initiator1 -clk ACLK -rst ARESET
uinb trig
uoutb done
cthread main_thread -reset_header -wait_header
master.in
void master::main_thread() {
…
while (1) {
//please write here
…
}
src/master.cpp
Implementation by designer
ssgen.pl -in master.in

## Slide 19
1.2.2. Generation of AXI slave i/F
AXI3/4 Slave I/F generation:
    Descriptions in module header file:
module test
clock ACLK
sreset ARESET pos
axi3/4_slave target1 -clk ACLK -rst ARESET
uint data_array[100]
cthread main_thread -reset_header -wait_header
test.in
src/test.h
…
#include “axi3/4_traits.h“
class test : public sc_module, public bus_fw_nb_put_get_if<1, axi3/4_def_traits::tlm_traits> {
public:
sc_in_clk ACLK;
sc_in<bool> ARESET;
target1_t target1;
SC_HAS_PROCESS(test);
SC_CTOR(test)
: ACLK(“ACLK")
…
, target1(“target1”)
, target1_adaptor(“target1_adaptor”)
{
target1.clk_rst(ACLK, ARESET);
target1.target_port(target1_adaptor);
target1_adaptor.target_port(*this);
…
}
(cont.)
virtual bool nb_put_awchan(const awchan_t& awchan, tag<1>* t);
virtual bool nb_can_put_awchan(tag<1>* t = 0) const;
virtual void reset_nb_put_awchan(tag<1>* t = 0) {}
virtual bool nb_put_wchan(const wchan_t& wchan, tag<1>* t = 0);
virtual bool nb_can_put_wchan(tag<1>* t = 0) const;
virtual void reset_nb_put_wchan(tag<1>* t = 0 );
virtual bool nb_get_bchan(bchan_t& bchan, tag<1>* t = 0);
virtual bool nb_can_get_bchan(tag<1>* t = 0) const;
virtual void reset_nb_get_bchan(tag<1>* t = 0);
virtual bool nb_put_archan(const archan_t& archan, tag<1>* t);
virtual bool nb_can_put_archan(tag<1>* t = 0) const;
virtual void reset_nb_put_archan(tag<1>* t = 0);
virtual bool nb_get_rchan(rchan_t& rchan, tag<1>* t);
virtual bool nb_can_get_rchan(tag<1>* t = 0) const;
virtual void reset_nb_get_rchan(tag<1>* t = 0);
Update v1.1

## Slide 20
1.2.2. Generation of AXI3 slave i/F
AXI3/4 Slave I/F generation: (cont.)
    Descriptions in module implementation file
bool test:: nb_put_awchan(const awchan_t& awchan, tag<1>* t)
{
bool rtn = true;
// please write here
return rtn;
}
bool test::nb_can_put_awchan(tag<1>* t = 0) const
{
bool rtn = true;
// please write here
return rtn;
}
void test:: reset_nb_put_awchan(tag<1>* t = 0)
{
//please write here
}
bool test:: nb_put_wchan(const wchan_t& wchan, tag<1>* t = 0) {…}
bool test:: nb_can_put_wchan(tag<1>* t = 0) const {..}
void test:: reset_nb_put_wchan(tag<1>* t = 0 ) {..}
bool test:: nb_get_bchan(bchan_t& bchan, tag<1>* t = 0) {..}
bool test:: nb_can_get_bchan(tag<1>* t = 0) const {..}
void test:: reset_nb_get_bchan(tag<1>* t = 0) {..}
bool test:: nb_put_archan(const archan_t& archan, tag<1>* t) {..}
bool test:: nb_can_put_archan(tag<1>* t = 0) const {..}
void test:: reset_nb_put_archan(tag<1>* t = 0) {..}
bool test:: nb_get_rchan(rchan_t& rchan, tag<1>* t) {..}
bool test:: nb_can_get_rchan(tag<1>* t = 0) const {..}
void test:: reset_nb_get_rchan(tag<1>* t = 0) {..}
module test
clock ACLK
sreset ARESET pos
axi3/4_slave target1
uint data_array[100]
cthread main_thread -reset_header -wait_header
test.in
ssgen.pl -in test.in
Similar generation as previous virtual function
Update v1.2
src/test.cpp

## Slide 21
Page 21
1. Generation of SC using AXI/APB4 Stratus SC library
For hierarchy mode: master I/F. Similar generated code for both AXI/APB4 bus.
Example of “tap” command using
module test
clock PCLK
sreset PRESET pos
apb4_master initiator1
cthread main_thread -reset_header -wait_header
test.in
top test_top
sub test.in test0
test_top.in
module test_top
clock PCLK
sreset PRESET pos
apb4_master initiator1
mod_test_top.in
module test
clock PCLK
sreset PRESET pos
apb4_master initiator1 -clk PCLK -rst PRESET
cthread main_thread -reset_header -wait_header
test.in
top test_top
sub test.in test0
tap test0.initiator1 top_initiatiator1
test_top.in
module test_top
clock PCLK
sreset PRESET pos
apb4_master top_initiator1
…
SC_MODULE(test_top) {
test test0;
hier_initiator1_t initiator1;
SC_CTOR(top)
: PCLK("PCLK")
, ...
, initiator1(“initiator1")
{
initiator1.hier_bind(test0.initiator1);
…
}
test_top.h
…
SC_MODULE(test_top) {
test test0;
hier_initiator1_t top_initiator1;
SC_CTOR(top)
: PCLK("PCLK")
, ...
, top_initiator1(“top_initiator1")
{
top_initiator1.hier_bind(test0.initiator1);
…
}
test_top.h
mod_test_top.in
Update v1.1

## Slide 22
Page 22
1. Generation of SC using AXI/APB4 Stratus SC library
For hierarchy mode: slave I/F. Similar generated code for both AXI/APB4 bus.
module test
clock PCLK
sreset PRESET pos
apb4_slave target1
cthread main_thread -reset_header -wait_header
test.in
top test_top
sub test.in test0
test_top.in
#include “test.h”
SC_MODULE(test_top) {
test test0;
hier_target1_t target1;
SC_CTOR(top)
: PCLK("PCLK")
, ...
, target1("target1")
{
target1.hier_bind(xf0.target1);
…
}
test_top.h
module test
clock PCLK
sreset PRESET pos
apb4_slave target1 -clk PCLK -rst PRESET
cthread main_thread -reset_header -wait_header
test.in
top test_top
sub test.in test0
tap test0.target1 top_target1
test_top.in
#include “test.h”
SC_MODULE(test_top) {
test test0;
hier_target1_t top_target1;
SC_CTOR(top)
: PCLK("PCLK")
, ...
, top_target1("top_target1")
{
top_target1.hier_bind(xf0.target1);
…
}
test_top.h
module test_top
clock PCLK
sreset PRESET pos
apb4_slave target1
mod_test_top.in
module test_top
clock PCLK
sreset PRESET pos
apb4_slave top_target1
mod_test_top.in
Update v1.1

## Slide 23
Page 23
1. Generation of SC using AXI/APB4 Stratus SC library
Module configuration: DUT master – TB slave, or DUT slave – TB master
The following is example for APB4. Similar generation code for AXI I/F. (Refer to sample data).
module test
clock PCLK
sreset PRESET pos
apb4_slave target1 -clk PCLK -rst PRESET
cthread main_thread -reset_header -wait_header
test.in
…
#ifdef _IES_ABVIP
#include "monitor.h“
#endif
int sc_main(int argc, char *argv[]) {
…
test test0(“test0”);
tb_test tb_test0(“tb_test0”);
#ifdef _IES_ABVIP
monitor monitor0("monitor0");
#endif
…
apb4_channel<apb4_def_traits> apb4_slave_channel (“apb4_slave_channel");
#ifndef _MODE_RTL
apb4_slave_channel(test0.target1);
#else
test0.target1_PADDR (apb4_slave_channel.PADDR );
test0.target1_PSELX (apb4_slave_channel.PSELX );
test0.target1_PENABLE(apb4_slave_channel.PENABLE);
test0.target1_PWRITE (apb4_slave_channel.PWRITE );
test0.target1_PWDATA (apb4_slave_channel.PWDATA );
test0.target1_PSTRB (apb4_slave_channel.PSTRB);
test0.target1_PPROT (apb4_slave_channel.PPROT);
test0.target1_PRDATA (apb4_slave_channel.PRDATA );
test0.target1_PREADY (apb4_slave_channel.PREADY );
test0.target1_PSLVERR(apb4_slave_channel.PSLVERR);
#endif
main_test.cpp
tb_test0.initiator1(apb4_slave_channel);
#ifdef _IES_ABVIP
monitor0.PCLK(PCLK);
monitor0.PRESET(PRESET);
monitor0.paddr(dut_to_master.PADDR);
monitor0.psel(dut_to_master.PSELX);
monitor0.penable(dut_to_master.PENABLE);
monitor0.pwrite(dut_to_master.PWRITE);
monitor0.pwdata(dut_to_master.PWDATA);
monitor0.prdata(dut_to_master.PRDATA);
monitor0.pready(dut_to_master.PREADY);
monitor0.pslverr(dut_to_master.PSLVERR);
monitor0.pstrb(dut_to_master.PSTRB);
monitor0.pprot(dut_to_master.PPROT);
#endif
main_test.cpp

## Slide 24
Page 24
1. Generation of SC using AXI/APB4 Stratus SC library
monitor.v module generation:
    For APB4: (similar to monitor.v in APB4 example)
module monitor (PCLK, PRESET, psel, …, prdata, pslverr );
parameter ABUS_WIDTH = 32; // Size of Address field
parameter DBUS_WIDTH = 32; // Size of Data field
parameter PSEL_N = 1; // Number of slaves present, i.e. width of psel signal;
// When configured as master (verifying a slave); leave PSEL_N as default of 1.
// When configured as slave (verifying a master);
// set PSEL_N to the number of slaves connected to the bus;
parameter PROT_WIDTH = 2;
parameter COVERAGE_ON = 0; // Set to 1: Enable functional covers
parameter MAX_WAIT_CYCLES_ON = 0; // Set to 1: Enable checking of PREADY within a fixed N cycles
parameter MAX_WAIT_CYCLES = 2; // Maximum wait cycles when PREADY goes high after PVALID;
// Value of 0 means no wait states, i.e. PREADY is always high
parameter RST_CHECKS_ON = 0; // Set to 1: Enable reset checks
parameter RECM_CHECKS_ON = 0; // Set to 1: Enable APB4 recommended checks
parameter XCHECKS_ON = 0; // Set to 1: Enable APB4 X-checks
parameter CONFIG_CSR_INTERFACE = 0; // Set to 1: Enable ABVIP to connect with CSR-PA checker
// Continuation
input PCLK;
input PRESET;
input [PSEL_N-1:0] psel; // Master select line
…
input [DBUS_WIDTH-1:0] prdata; // Slave read data
input pslverr; // Slave error signal
cdn_abvip_apb4_monitor #(
.ABUS_WIDTH (ABUS_WIDTH ),
.DBUS_WIDTH (DBUS_WIDTH ),
.PSEL_N (PSEL_N ),
….
) apb4_monitor (
.pclk (PCLK),
.presetn (!PRESET),
.psel (psel ),
….
.prdata (prdata ),
.pslverr (pslverr)
);
endmodule
Add v1.1

## Slide 25
Page 25
1. Generation of SC using AXI/APB4 Stratus SC library
monitor.v module generation:
    For AXI3: (similar to monitor.v in AXI3 example)
// Continuation
input ACLK;
input ARESET;
input [ID_WIDTH-1:0] awid;
input [ADDR_WIDTH-1:0] awaddr;
...
input rready;
cdn_abvip_axi4_monitor #(
.ADDR_WIDTH (ADDR_WIDTH ),
.DATA_WIDTH (DATA_WIDTH ),
...
.LOW_POWER_ON(LOW_POWER_ON)
) axi_monitor (
.aclk (ACLK), .aresetn (!ARESET),
.awid (awid), .awaddr (awaddr),
...
.rvalid (rvalid), .rready (rready),
.csysreq (1’b0),
.csysack (1’b0),
.cactive (1’b0)
);
endmodule
Add v1.1
module monitor(ACLK, ARESET, awid, awaddr, ... rready);
parameter ADDR_WIDTH = 32;
parameter DATA_WIDTH = 64;
parameter ID_WIDTH = 4;
parameter LEN_WIDTH = 4;
parameter SIZE_WIDTH = 4;
parameter BURST_WIDTH = 2;
parameter LOCK_WIDTH = 2;
parameter CACHE_WIDTH = 4;
parameter PROT_WIDTH = 3;
parameter BRESP_WIDTH = 2;
parameter RRESP_WIDTH = 2;
parameter COVERAGE_ON = 1;
parameter RST_CHECKS_ON = 1;
parameter X_CHECKS_ON = 1;
parameter MAX_WAIT_CYCLES_ON = 1;
parameter ALL_STROBES_HIGH_ON = 0;
parameter BYTE_STROBE_ON = 1;
parameter EXCL_ACCESS_ON = 1;
parameter LOCKED_ACCESS_ON = 1;
parameter READ_INTERLEAVE_ON = 0;
parameter WRITE_INTERLEAVE_ON = 0;
parameter READ_RESP_IN_ORDER_ON = 1;
parameter WRITE_RESP_IN_ORDER_ON = 1;
parameter LOW_POWER_ON = 1;
Value is corresponding to specified value of “apb4/axi3/axi4_master/slave command’s options

## Slide 26
Page 26
1. Generation of SC using AXI/APB4 Stratus SC library
monitor.v module generation:
    For AXI4: (similar to monitor.v in AXI4 example)
// Continuation
…
input [ID_WIDTH-1:0] awid;
input awlock;
input [QOS_WIDTH-1:0] awqos;
input [REGION_WIDTH-1:0] awregion;
input [AWUSER_WIDTH-1:0] awuser;
input [ADDR_WIDTH-1:0] awaddr;
...
input rready;
cdn_abvip_axi4_monitor #(
.ADDR_WIDTH (ADDR_WIDTH ),
.DATA_WIDTH (DATA_WIDTH ),
...
.LOW_POWER_ON(LOW_POWER_ON)
) axi_monitor (
.aclk (ACLK), .aresetn (!ARESET),
.awid (awid), .awaddr (awaddr),
...
.cactive (1’b0)
);
endmodule
Add v1.1
module monitor(ACLK, ARESET, awid, awaddr, ... rready);
parameter ADDR_WIDTH = 32;
parameter DATA_WIDTH = 64;
parameter ID_WIDTH = 4;
parameter LEN_WIDTH = 8;
parameter SIZE_WIDTH = 4;
…
parameter AWUSER_WIDTH = 32; // Size of AWUser field
parameter WUSER_WIDTH = 32; // Size of WUser field
parameter BUSER_WIDTH = 32; // Size of BUser field
parameter ARUSER_WIDTH = 32; // Size of ARUser field
parameter RUSER_WIDTH = 32; // Size of RUser field
…
parameter LOW_POWER_ON = 1;
Value is corresponding to specified value of “apb4/axi3/axi4_master/slave command’s options

## Slide 27
Page 27
1. Generation of SC using AXI/APB4 Stratus SC library
.map module generation: monitor_ies.map, <module>_ies.map
    The following is example of APB4 I/F. The corresponding declaration will be generated for AXI3/AXI4.
-sctype "PCLK:bool"
-sctype "PRESET:bool"
-sctype "trig:bool"
-sctype "INT:bool"
-sctype "target1_PADDR:sc_uint<32>"
-sctype "target1_PSELX:sc_uint<1>"
-sctype "target1_PENABLE:bool"
-sctype "target1_PWRITE:bool"
-sctype "target1_PWDATA:sc_uint<32>"
-sctype "target1_PSTRB:sc_uint<4>"
-sctype "target1_PPROT:sc_uint<3>"
-sctype "target1_PRDATA:sc_uint<32>"
-sctype "target1_PREADY:bool"
-sctype "target1_PSLVERR:bool"
Add v1.1
-sctype "PCLK:bool"
-sctype "PRESET:bool"
-sctype "paddr:sc_uint<32>"
-sctype "psel:sc_uint<1>"
-sctype "penable:bool"
-sctype "pwrite:bool"
-sctype "pwdata:sc_uint<32>"
-sctype "pstrb:sc_uint<4>"
-sctype "pprot:sc_uint<3>"
-sctype "prdata:sc_uint<32>"
-sctype "pready:bool"
-sctype "pslverr:bool"
monitor_ies.map
test_ies.map
Channel name
Depended on I/F command option in any

## Slide 28
Page 28
1. Generation of SC using AXI/APB4 Stratus SC library
Module configuration: DUT master – DUT slave. The following is example for APB4. Similar generation code for AXI I/F.
module master
clock PCLK
sreset PRESET pos
apb4_master initiator1
cthread main_thread -reset_header -wait_header
master.in
#include “master.h”
#include “slave.h”
SC_MODULE(top) {
master master0;
slave slave0;
apb4_channel<apb4_def_traits> master0_to_slave0;
SC_CTOR(top)
: PCLK("PCLK")
, ...
, master0(“master0")
, slave0(“slave0”)
, master0_to_slave0 (“master0_to_slave0 ")
{
master0_to_slave0(slave0.target1);
master0.initiator1(master0_to_slave0);
}
top.h
module slave
clock PCLK
sreset PRESET pos
apb4_slave target1 -clk PCLK -rst PRESET
cthread main_thread -reset_header -wait_header
slave.in
module top
sub master master0
sub slave slave0
bind master0.initiator1 slave0.target1 master0_to_slave0
top.in

## Slide 29
Page 29
2. Preprocessor support for “bind” and “mem”
Request from RVC/VideoIP: Support only #ifdef, #endif for “bind” and “mem” only (not support “#else”, #ifndef, #if, nested #ifdef). And user should assure the preprocessor description by themselves to avoid “port not bound” error.
If preprocessor is defined for “bind”, “mem”: the preprocessor will be generated to the corresponding code. (Auto-bind generation code will be not generated)
top test_top
sub test.in test0
sub testa.in test1
#ifdef MACRO_DEF
bind test0.port_sync test1.port_sync port_sync
#endif
#ifdef MACRO_DEF_A
bind 0 test0.port_sync sig_tmp
#endif
SC_MODULE(test_top) {
#ifdef MACRO_DEF
sc_signal < bool > port_sync;
#endif
#ifndef MACRO_DEF
sc_signal < bool > sig_tmp;
#endif
…
SC_CTOR(test_top)
..
#ifdef MACRO_DEF
, port_sync(" port_sync")
#endif
#ifndef MACRO_DEF
, sig_tmp("sig_tmp")
#endif
…
(cont.)
#ifdef MACRO_DEF
sc_signal < bool > port_sync;
#endif
#ifdef MACRO_DEF
test0.port_sync(port_sync);
#endif
#ifndef MACRO_DEF
test0.port_sync(sig_tmp);
#endif
void method_fixed() {
#ifndef MACRO_DEF
sig_tmp.write(0);
#endif
}
}
testx.port_sync will be recognized as “binded” (not generate code in main)

## Slide 30
Page 30
3. fix `struct` issues
3.1 Fix SLEC ISSUE
Similar to discussion through email. Generated code in .tcl file should be revised.
foreach io {-input -output} {
foreach spec_var [find -port -spec $io -short_name -regexp {.*[[0-9]+].*|.*\..*}] {
set impl_var [regsub -all {\.} $impl_var {_}]
...
foreach spec_var [find -inst -sequential -spec -short_name -regexp {.*[[0-9]+].*|.*\..*}] {
set impl_var [regsub -all {\.} $impl_var {_}]
slec_*_st.tcl

## Slide 31
Page 31
3. fix `struct` issues
3.1 Fix SLEC ISSUE
Similar to discussion through email. Add the following code in tcl file:
set bbox_list [findlist -inst -blackbox spec.* -require impl.%1]
set expr_list {
*[*] %1_%2
*[*][*] %1_%2_%3
*[*][*][*] %1_%2_%3_%4
*.* %1_%2
*.*[*] %1_%2_%3
*.*[*][*] %1_%2_%3_%4
*.*[*][*][*] %1_%2_%3_%4_%5
*[*].* %1_%2_%3
*[*].*[*] %1_%2_%3_%4
*[*].*[*][*] %1_%2_%3_%4_%5
*[*][*].* %1_%2_%3_%4
*[*][*].*[*] %1_%2_%3_%4_%5
*[*][*][*].* %1_%2_%3_%4_%5
}
slec_*_st.tcl
foreach {spec_bbox impl_bbox} $bbox_list {
foreach io {-input -output} {
set io_inv "-output"
if { $io == "-output" } {
set io_inv "-input"
}
foreach { spec_expr impl_expr } $expr_list {
set p_list [findlist -port $io $spec_bbox.$spec_expr -require $impl_bbox.$impl_expr]
foreach { spec_port impl_port } $p_list {
create_map $io_inv $spec_port $impl_port
}
}
}
}

## Slide 32
Page 32
3. fix `struct` issues
3.2 Fix sim_eq ISSUE
If “-sim_eq” is used: generate code for both RTL and struct port in tb_dut, stimulus, main_dut_eq (not change from “sim_eq” example).
struct Package {
uvarb vld
uvar8 data
uvar4 d2[2]
}
module dut
clock clk
sreset rst pos
uinb din_en
uinPackage din
uoutb dout_en
uoutPackage dout
cthread main_thread -reset_header
dut.in
Package m_din;
Package m_dout_s;
Package m_dout_r;
….
#ifndef _MODE_RTL
din.write(Package());
#else
din_vld.write(0);
din_data.write(0);
din_d2_0.write(0);
din_d2_1.write(0);
#endif
…
void my_wait() {
#ifndef _MODE_RTL
din.write(m_din);
#else
…
#endif
wait();
#ifndef _MODE_RTL
m_dout = dout.read();
#else
…
#endif
}
tb_dut_eq.h
Package v_dout_s = dout_s.read();
fprintf(scout0, " %08x" , v_dout_s.to_uint());
fprintf(scout0, " %08x" , v_dout_s.vld);
fprintf(scout0, " %08x" , v_dout_s.data.to_uint());
for (int i0 = 0; i0 < 2; i0++) {
fprintf(scout0, " %08x" , v_dout_s.d2[i0].to_uint());
}
…
Package v_dout_r = dout_r.read();
fprintf(rtlout0, " %08x" , v_dout_r.to_uint());
bool v_dout_vld_r = dout_vld_r.read();
fprintf(rtlout0, " %08x" , v_dout_vld_r);
sc_uint<8> v_dout_data_r = dout_data_r.read();
fprintf(rtlout0, " %08x" , v_dout_data_r.to_uint());
sc_uint<4> v_dout_d2_r[2];
v_dout_d2_r[0] = dout_d2_0_r.read();
fprintf(rtlout0, " %08x" , v_dout_d2_r[0].to_uint());
v_dout_d2_r[1] = dout_d2_1_r.read();
fprintf(rtlout0, " %08x" , v_dout_d2_r[1].to_uint());
tb_dut_eq.cpp
Update v1.2

## Slide 33
Page 33
3. fix `struct` issues
3.2 Fix sim_eq ISSUE
If “-sim_eq” is used: generate code for both RTL and struct port in tb_dut, stimulus, main_dut_eq (not change from “sim_eq” example).
struct Package {
uvarb vld
uvar8 data
uvar4 d2[2]
}
module dut
clock clk
sreset rst pos
uinb din_en
uinPackage din
uoutb dout_en
uoutPackage dout
cthread main_thread -reset_header
dut.in
v_din = rand()%1;
v_din.vld = rand()%2;
v_din.data = rand()%256;
for (int i0 = 0; i0 < 2; i0++) {
v_din.d2[i0] = rand()%16;
}
din_vld.write(v_din.vld);
din_data.write(v_din.data);
din_d2_0.write(v_din.d2[0]);
din_d2_1.write(v_din.d2[1]);
...
v_din = rand()%1;
v_din.vld = rand()%2;
v_din.data = rand()%256;
for (int i0 = 0; i0 < 2; i0++) {
v_din.d2[i0] = rand()%16;
}
din_vld.write(v_din.vld);
din_data.write(v_din.data);
din_d2_0.write(v_din.d2[0]);
din_d2_1.write(v_din.d2[1]);
stimulus.h
tb_dut_eq0.din_vld(din_vld);
tb_dut_eq0.din_data(din_data);
tb_dut_eq0.din_d2_0(din_d2_0);
tb_dut_eq0.din_d2_1(din_d2_1);
…
tb_dut_eq0.dout_r(dout_r);
tb_dut_eq0.dout_vld_r(dout_vld_r);
tb_dut_eq0.dout_data_r(dout_data_r);
tb_dut_eq0.dout_d2_0_r(dout_d2_0_r);
tb_dut_eq0.dout_d2_1_r(dout_d2_1_r);
main_dut_eq.cpp
Update v1.2