## Slide 1
SSGEN enhancement Specification
2018Q2
2018 May 14
FRONTEND DESIGN 2 Department
RENESAS DESIGN VIETNAM

## Slide 2: contents
New command “separate_scmain_file” Page 03
Support “cthread” in “`ifdef TESTBENCH” Page 07
New command line option “-vwrap” Page 09
Support VideoIP request Page 11
Other enhancements Page 13

## Slide 3: NEW command “separate_scmain_file” (1/4)
  Syntax: separate_scmain_file {on|off}
    off: default
      main_*.cpp is outputted as before.
    on: two files are outputted (main_*.cpp and main_*.hpp)
      main_*.hpp
        Memory allocation, module instantiations, signal declarations and connections are outputted in this file.
        File overwrite rule is same as *.h files.
      main_*.cpp
        Remaining descriptions are outputted in this file.
        This file includes “main_*.hpp”.
        File overwrite rule is same as *cpp files.

## Slide 4: NEW command “separate_scmain_file” (2/4)
  Command order: must be specified before “module/top” command.
  Command scope:
    Can be specify in included file.
    Can be specify under “`if/`ifdef/`else/`elif” except for TESTBENCH, SLEC_BBOX and _DEBUG_* macros.
    Cannot be specified under “#ifdef”
  For hierarchy mode:
    Must be specified in top module. Commands specified in sub-module have no effect for top module.

## Slide 5: NEW command “separate_scmain_file” (3/4)
  Example – module generation mode
separate_scmain_file on
module test
clock clk
sreset rst pos
…
test.in
// main_test.cpp
#include "test.h"
#include "tb_test.h"
int sc_main(int argc, char *argv[]) {
…
printf("clk: %d ns …);
#include "main_test.hpp"
ssgen_trace_file*tf= NULL;
…
return 0;
}
// main_test.hpp
test test0("test0");
tb_testtb_test0("tb_test0");
sc_signal< bool > rst;
sc_signal< bool > in0;
sc_signal< bool > out0;
test0.clk(clk);
…
test0.out0(out0);
tb_test0.clk(clk);
…
tb_test0.out0(out0);
main_test.cpp
main_test.hpp

## Slide 6: NEW command “separate_scmain_file” (4/E)
  Example – hierarchy generation mode
top test_top
sub test.in t0
…
separate_scmain_file on
module test
clock clk
sreset rst pos
…
test.in
test_top.in
// main_test_top.cpp
#include "test_top.h"
#include "tb_test_top.h"
int sc_main(int argc, char *argv[]) {
…
printf("clk: %d ns …);
test_top test_top0("test_top0");
tb_test_top tb_test_top0("tb_test_top0");
sc_signal< bool > rst;
…
ssgen_trace_file*tf= NULL;
…
return 0;
}
main_test_top.cpp
No effect

## Slide 7: Support “cthread” in “`ifdef TESTBENCH” (1/2)
  When “cthread” is specified inside “`ifdef TESTBENCH”, descriptions of specified SC_CTHREAD are generated in TB in addition to thread_main.
module test
clock clk
sreset rst pos
…
`ifdef TESTBENCH
cthread thread_sub
`endif
test.in
#include <systemc.h>
#include "ssgenlib.h“
SC_MODULE(tb_test) {
…
SC_CTOR(tb_test)
{
SC_CTHREAD(thread_main, clk.pos());
SC_CTHREAD(thread_sub, clk.pos());
reset_signal_is(rst, true);
}
…
};
#include "tb_test.h"
void tb_test::thread_main() {
…
}
void tb_test::thread_sub() {
wait();
while(1) {
// please write here!
wait();
}
}
tb_test.h
tb_test.cpp

## Slide 8: Support “cthread” in “`ifdef TESTBENCH” (2/E)
  In hierarchy generation mode, “cthread” command is only allowed inside `ifdef TESTBENCH
    Option “-clk” and “-rst” can be used to specify clock and reset signal respectively. If not specified, first defined clock/reset signal will be used. If there is no valid clock, dummy clock is used.
    Other options are not supported (error will be outputted if specified).
top test_top
sub test1.in t1
sub test2.in t2
`ifdef TESTBENCH
cthread thread_sub -clk clk2 –rst rst1
`endif
module test1
clock clk1
sreset rst1 pos
…
test1.in
test_top.in
module test2
clock clk2
sreset rst2 pos
…
test2.in
#include <systemc.h>
#include "ssgenlib.h“
SC_MODULE(tb_test_top) {
…
SC_CTOR(tb_test_top)
{
SC_CTHREAD(thread_main, clk1.pos());
SC_CTHREAD(thread_sub, clk2.pos());
reset_signal_is(rst1, true);
}
…
};
tb_test_top.h

## Slide 9: New command line option “-vwrap” (1/2)
  When “-vwrap” is specified, SSGEN outputs Verilog wrapper file.
    File name: xxx_wrap.v (“module test” -> test_wrap.v, “top test_top” -> test_top_wrap.v)
    Module name: xxx_wrap (“module test” -> test_wrap, “top test_top” -> test_top_wrap)
    Verilog wrapper module has same input and output ports with SystemC module
    Verilog wrapper instantiates SystemC module.

## Slide 10: New command line option “-vwrap” (2/E)
  Examples
module test
uinb in0
uoutb out0[2]
test.in
module test_wrap(in0, out0);
input in0;
output out0 [1:0];
test test0(.in0(in0), .out0 (out0));
endmodule
-vwrap
test_wrap.v
top test_top
sub test.in t0
test_top.in
module test_top_wrap(in0, out0);
input in0;
output out0 [1:0];
test_top test_top0(.in0(in0), .out0 (out0));
endmodule
-vwrap
test_top_wrap.v

## Slide 11: Support VideoIP request (1/2)
  Support to generate are number of ports/signals with same prefix by adding a new option “-num” to {u|s}{in|out} commands.
`define MAX 3
module modA
uinb in -num MAX
modA.in
#include <systemc.h>
#include "ssgenlib.h“
SC_MODULE(modA) {
…
sc_uint< bool > in0;
sc_uint< bool > in1;
sc_uint< bool > in2;
…
};
modA.h

## Slide 12: Support VideoIP request (2/E)
  Purpose: SSGEN does not support to bind single element of a port array. By this way “bind” command can be specified for each single port.
module modA
uinb in -num 3
modA.in
module modB
uoutb out -num 2
modB.in
module modC
uinb out -num 3
modC.in
top top
sub modA.in modA0
sub modA.in modA1
sub modB.in modB0
sub modC.in modC0
bind modB0.out0 modA0.in0 sig0
bind modB0.out1 modA0.in1 sig1
bind 0 modA0.in2 fix0
bind modC0.out0 modA1.in0 sig2
bind modC0.out1 modA1.in1 sig3
bind modC0.out2 modA1.in2 sig4
top.in
This cannot be done using port array

## Slide 13: Other enhancements (1/2)
  Remove W003 message
  Support new command line option “-nst” to not stop SSGEN due to ERROR.
    SSGEN will output as many errors messages as possible.
    No output file will be generated due to ERROR.
  Change simulator version
    VCS and vcs_gcc 2016.06-sp2 -> 2017.03-sp2
    IES: migrate to Xcelium 17.04.004

## Slide 14: Other enhancements (2/E)
  Fix problem about “-slec_bbox” in “func”.
  Change pipeline constrain directive for Stratus
…
func void func0() -slec_bbox
test.in
…
set_attr dont_ungroup_name "test_func0_*" ;
project_test.tcl
…
cthread main_thread -pipe -pipe_max 4
test.in
…
HLS_CONSTRAIN_LATENCY(0, 4, PL_MAIN_CONST_main_thread);
test.cpp
…
cthread main_thread -pipe
test.in
…
HLS_CONSTRAIN_LATENCY(0, HLS_ACHIEVABLE, PL_MAIN_CONST_main_thread);
test.cpp

## Slide 15
Renesas.com
Rev | Contents | Approved by | Checked by | Created by
1.0 | Newly created |  | Yen Nguyen 2018/05/11 | Hiep Nguyen 2018/05/11